## Slide 1: AVR Timer 0 Programming
Dr.Sreejith Rajan

## Slide 2: AVR Timer 0
8-bit timer/counter
Normal mode and CTC Mode
TCNT0,TCCR0,TIFR and OCR0

## Slide 3: Delay Function
Let us create a delay function using TIMER 0 in Normal Mode

## Slide 4: TCNT0
Load TCNT0 with initial value

## Slide 5: TCCR0
0
1
FOC → Force Output Compare
COM → Compare Output Mode
WGM → Waveform Generation Mode
CS → Clock Select/Presclar

## Slide 6: TCCR0A &TCCR0B
From the ATmega328 datasheet
TCCR0A – Timer/Counter Control Register A
  8 bit register
  Bits: COM0A1, COM0A0, COM0B1, COM0B0, –, –, WGM01, WGM00
TCCR0B – Timer/Counter Control Register B
  8 bit register
  Bits: FOC0A, FOC0B, –, –, WGM02, CS02, CS01, CS00

## Slide 7: TCCR0A & TCCR0B
Summary for ATmega328
You use them together to configure Timer0:
  Mode selection (Normal, CTC, Fast PWM, etc.) → WGM02:0 across A & B
  Compare output control (OC0A / OC0B pin actions) → in TCCR0A
  Prescaler / clock source → in TCCR0B
That’s why in code, you’ll often see both registers being written when setting up Timer0.
1

## Slide 8: TIFR(Timer/Counter Interrupt Flag Register
0
1

## Slide 9: The undigested TIFR0 |= (1 << TOV0);
Hardware sets it to 1 whenever Timer0 overflows (goes from 255 → 0).
To clear it, you must write a 1 to it
(yes, opposite of normal thinking!).
Writing 0 has no effect.
0
1

## Slide 10: Everything else is NORMAL
Overflow Check Command
while (!(TIFR0 & (1 << TOV0))); // wait until overflow
0
1

## Slide 11: Lets Write some code
0
1

## Slide 12
THANK YOU