## Slide 1: Interrupts in Atmega328
Dr.Sreejith Rajan

## Slide 2: Interrupts
An interrupt is a sudden event that pauses the normal execution of a program and forces the CPU to temporarily run a special piece of code (ISR – Interrupt Service Routine), after which the CPU returns to where it left off.
1

## Slide 3: Types of Interrupts (atmega328)
External Interrupts : Triggered by signals on external pins.
  INT0 → Pin PD2
  INT1 → Pin PD3
Pin Change Interrupts (PCINT):
  PCINT0–7 → Port B (PB0–PB7)
  PCINT8–14 → Port C (PC0–PC6)
  PCINT16–23 → Port D (PD0–PD7)
1

## Slide 4: Types of Interrupts (atmega328)
2. Timer/Counter Interrupts
Timer0 (8-bit)
  Compare Match A (TIMER0_COMPA_vect)
  Compare Match B (TIMER0_COMPB_vect)
  Overflow (TIMER0_OVF_vect)
Timer1 (16-bit)
  Capture Event (TIMER1_CAPT_vect)
  Compare Match A (TIMER1_COMPA_vect)
  Compare Match B (TIMER1_COMPB_vect)
  Overflow (TIMER1_OVF_vect)
Timer2 (8-bit)
  Compare Match A (TIMER2_COMPA_vect)
  Compare Match B (TIMER2_COMPB_vect)
  Overflow (TIMER2_OVF_vect)
1

## Slide 5: Types of Interrupts (atmega328)
3. Peripheral Interrupts
  USART
  SPI
  ADC
  I2C
  Analog Comparator
  EPROM Ready
1

## Slide 6: Types of Interrupts (atmega328)
4. System Interrupts
  RESET
  Watchdog Timer(If enabled)

## Slide 7: Interrupt Programming
Program is running normally
Interrupt happens
CPU pauses current execution and jump to the corresponding Interrupt Vector Table(IVT)-An address corresponding to each interrupt
IVT Contains the address of the corresponding Interrupt Service Routine.
CPU Executes ISR and return to the original location where interrupt happened and resumes normal operation
1

## Slide 8: General Process of Interrupt Programming (ATmega328)
Step 1 – Enable Global Interrupts
Step 2 – Configure the Peripheral or Source
  Depending on the interrupt source:
    External interrupt (INT0/INT1) → configure EICRA (trigger type).
    Timer interrupt → configure TCCR0x/TCCR1x/TCCR2x (mode, prescaler).
    ADC/USART/etc. → configure their control registers.
1

## Slide 9: General Process of Interrupt Programming (ATmega328)
Step 3 – Enable the Interrupt in Mask Register
Each peripheral has its own Interrupt Mask Register:
  EIMSK → for external interrupts.
  TIMSK0/TIMSK1/TIMSK2 → for timers.
  ADCSRA → for ADC interrupt.
Setting the right bit tells the MCU: “Yes, allow this specific interrupt.”
1

## Slide 10: General Process of Interrupt Programming (ATmega328)
Step 4 – Write the ISR (Interrupt Service Routine)
  Define the function that should run when the interrupt occurs.

## Slide 11: General Process of Interrupt Programming (ATmega328)
Step 5 – Main Program Loop
1

## Slide 12: Timer Overflow Interrupt – A new register to learn
Bit | Name | Function
2 | OCIE0B | Output Compare Match B Interrupt Enable
1 | OCIE0A | Output Compare Match A Interrupt Enable
0 | TOIE0 | Overflow Interrupt Enable

## Slide 13: A register common to all interrupt programming - SREG
Bit 7 controls the interrupts : sei() enables it and cli() disables it

## Slide 14
THANK YOU