## Slide 1: AVR Timer 0 Programming
Dr.Sreejith Rajan

## Slide 2: AVR Timer 0
8-bit timer/counter
Normal mode and CTC Mode
TCNT0,TCCR0,TIFR and OCR0

## Slide 3: Delay Function
Let us create a delay function using TIMER 0 in Normal Mode

## Slide 4: TCNT0
Load TCNT0 with initial value

## Slide 5: TCCR0
0
1
FOC → Force Output Compare
COM → Compare Output Mode
WGM → Waveform Generation Mode
CS → Clock Select/Presclar

## Slide 6: TCCR0A &TCCR0B
From the ATmega328 datasheet
TCCR0A – Timer/Counter Control Register A
  8 bit register
  Bits: COM0A1, COM0A0, COM0B1, COM0B0, –, –, WGM01, WGM00
TCCR0B – Timer/Counter Control Register B
  8 bit register
  Bits: FOC0A, FOC0B, –, –, WGM02, CS02, CS01, CS00

## Slide 7: TCCR0A & TCCR0B
Summary for ATmega328
You use them together to configure Timer0:
  Mode selection (Normal, CTC, Fast PWM, etc.) → WGM02:0 across A & B
  Compare output control (OC0A / OC0B pin actions) → in TCCR0A
  Prescaler / clock source → in TCCR0B
That’s why in code, you’ll often see both registers being written when setting up Timer0.
1

## Slide 8: TIFR(Timer/Counter Interrupt Flag Register
0
1

## Slide 9: The undigested TIFR0 |= (1 << TOV0);
Hardware sets it to 1 whenever Timer0 overflows (goes from 255 → 0).
To clear it, you must write a 1 to it
(yes, opposite of normal thinking!).
Writing 0 has no effect.
0
1

## Slide 10: Everything else is NORMAL
Overflow Check Command
while (!(TIFR0 & (1 << TOV0))); // wait until overflow
0
1

## Slide 11: Lets Write some code
0
1

## Slide 12: Load TCNT0 - IE Minimum value configure normal mode configure no prescaling configure loop (find out count for required delay) wait until the TOV0 flag is set reset TOV0 Flag Repeat loop until condition is violated
0
1

## Slide 13
THANK YOU